MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, Inc.

9036 Winnetka Ave.

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-------------------------------------CHEMICAL NAME:  Polymeric precursor for aluminum oxide

CATALOG NUMBER: ALO9401

TSCA:  not listed in the TSCA inventory.

CHEMICAL FAMILY: Polymeric metal organic oxoalkoxides.

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------HAZARDOUS INGREDIENTS:	%

2-methoxyethanol	~90%	ACGIH(TLV): 5 ppm

OSHA/PEL: 25 ppm

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE:  Light yellow liquid.

MELTING POINT: -85.1°C (2-methoxyethanol)	BOILING POINT: 124°C (2-methoxyethanol)

VAPOR PRESSURE: 6.22 mm Hg (@20°C)	SPECIFIC GRAVITY: No data

CRYSTALLIZATION TEMPERATURE:  No data

RESULTING PRODUCTS:  Al2O3 (Oxide content:  >1 wt%)

SOLUBILITY:  Soluble in 2-methoxyethanol, hexane, toluene.

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: N/A

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Dry chemical, carbon dioxide, water spray or regular foam.

SPECIAL FIRE FIGHTING PROCEDURES:  If involved in a fire or heated to high temperatures, the material may burn.  Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS:  No unusual fire or explosion hazards.

-----------------------------------------------HEALTH HAZARD-------------------------------------

MODE OF ENTRY:

INHALATION: No

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

Harmfull if swallowed or absorbed through skin.  Material is extremely destructive to tissue of the mucous membranes and upper respiratory tract, eyes, and skin.  Symptoms of exposure may include burning sensation, coughing, wheezing, laryngitis, shortness of breath, headache, nausea, and vomiting.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with ethanol first, then soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY: Stable.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Hydrolyzes with water.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, aluminum oxide, and organic fumes.

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS------------------------

VENTILATION REQUIREMENTS:  Fume hood recommended.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE:  Keep away from heat and excessive moisture.

OTHER PRECAUTIONS:  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

----------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: June, 2011