MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION--------------------------------------

CHEMICAL NAME: Indium 2-ethylhexanoate, in hexane

CATALOG NUMBER: I122

FORMULA: In(OOCC7H15)3	                FORMULA WEIGHT: 544.09

TSCA:  listed in the TSCA inventory

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound                                  10	ACGIH(TLV): 0.5mg In/m3

Hexane                                             90	OSHA/PEL: No data

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE : liquid

MELTING POINT: No data 	BOILING POINT: No data

VAPOR PRESSURE: No data 	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: insoluble

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: -9oF

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Use carbon dioxide or dry powder as extinguishing agents.

SPECIAL FIRE FIGHTING PROCEDURES: Burning material may release toxic and corrosive fumes. Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS:  No unusual fire or explosion hazards.

-----------------------------------------------HEALTH HAZARD-------------------------------------

MODE OF ENTRY:

INHALATION: No

SKIN CONTACT: No

EYE CONTACT: No

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

Indium compounds:  Indium compounds injected into experimental animals are found to be highly toxic.  Effect include reduced food and waterconsumption with accompanying weight loss, pulmonary edema, necrotizing pneumonia, blood damage, liver and kidney damage, hind leg paralysis in rabbits anddamge to the brain, heart, adrenals and spleen.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, 	shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of 	water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY: Air and moisture stable.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Oxidizing agents.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, barium oxide, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-----------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS-----------------------

VENTILATION REQUIREMENTS: Hood.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Store the material in a sealed containers.  Keep away from heat and moisture.

OTHER PRECAUTIONS: To minimize exposure handle the material in an efficient fume hood.No special precautions necessary.

------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  March 21, 1996