MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Neodymium 2-methoxyethoxide (in 2-methoxyethanol)

CATALOG NUMBER: N110	PURITY: 99%

FORMULA: Nd(OCH2CH2OCH3)3	FORMULA WEIGHT: 369.34

TSCA: not listed in the TSCA inventory	2-methoxyethanol: listed

CHEMICAL FAMILY: Metal alkoxide solution

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	16 	ACGIH(TLV): No data

OSHA/PEL: No data

2-Methoxyethanol	 84	ACGIH(TLV): 25ppm

OSHA/PEL: 25 ppm

------------------------------------------------PHYSICAL DATA-----------------------------------------------

MELTING POINT: No data	BOILING POINT: 124.5oC (2-methoxyethanol)

VAPOR PRESSURE: No data	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 115F (2-methoxyethanol)

AUTOIGNITION TEMPERATURE: 545F (2-methoxyethanol)

EXTINGUISHING MEDIA: Flammable liquid.  Use alcohol foam, carbon dioxide or dry chemical extinguishing agents.  Water may be used to keep fire exposed containers cool.

SPECIAL FIRE FIGHTING PROCEDURES: Flammable liquid.  Material readily ignited with flame, sparks, friction or heat.  Burning material may release toxic and corrosive fumes.  Vapors can flow along surfaces to distant ignition sources and flash back.  Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing..

UNUSUAL FIRE OR EXPLOSION HAZARDS: Keep away from all sources of ignition-no smoking

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

Neodymium: THR = HIGH via iv and ic routes.  It may be an anticoagulant lanthanon.  Care in handling is advised.  Neodymium metal has moderate fire hazard, in the form of dust, when exposed to heat or flame.  It can react violently with air, halogens, N2, P.

INHALATION: Harmful by inhalation.

SKIN CONTACT:Harmful.  Readily absorbs through skin.

EYE CONTACT: Irritating to the eyes.

INGESTION: Harmful.  Possible risk of impaired fertility.  May cause harm to the unborn child.

TARGET ORGANS: Blood, kidneys

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Moisture, heat, strong oxidizers, acid chlorides, acid anhydrides.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, neodymium oxide, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: Jan. 2015