MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Praseodymium 2-methoxyethoxide, in 2-methoxyethanol

CATALOG NUMBER: P310	PURITY: 99%

FORMULA: Pr(OCH2CH2OCH3)3	FORMULA WEIGHT: 366.01

TSCA: not listed in the TSCA inventory      2-methoxyethanol:  listed

CHEMICAL FAMILY: Metal alkoxide solution

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	5 	ACGIH(TLV): No data

OSHA/PEL: No data

2-methoxyethanol	 95	ACGIH(TLV): 5ppm

OSHA/PEL: 25ppm

---------------------------------------------------PHYSICAL DATA--------------------------------------------

APPEARANCE AND ODOR: Clear blue solution

MELTING POINT: -85oC (2-methoxyethanol)	BOILING POINT: 124-125oC (2-methoxyethanol)

VAPOR PRESSURE: No data		SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 115F (46oC) (2-methoxyethanol)

AUTOIGNITION TEMPERATURE: 545F (284oC) (2-methoxyethanol)

EXTINGUISHING MEDIA: Flammable liquid.  Use alcohol foam, carbon dioxide or dry chemical extinguishing agents.  Water may be used to keep fire exposed containers cool.

SPECIAL FIRE FIGHTING PROCEDURES: Flammable liquid.  Material readily ignited with flame, sparks, friction or heat.  Burning material may release toxic and corrosive fumes.  Vapors can flow along surfaces to distant ignition sources and flash back.  Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing..

UNUSUAL FIRE OR EXPLOSION HAZARDS: forms explosive mixture in air (2-methoxyethanol)

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

INHALATION: Vapor or mist is irritating to the eyes, mucous membranes and upper respiratory tract.

SKIN CONTACT: Readily absorbed through skin.

EYE CONTACT: Vapors may irritate the eyes.  Splashes may cause severe irritation, possible corneal burns and eye damage.

INGESTION: 2-methoxyethanol may cause harm to unborn child.  Possible risk of impaired fertility.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Moisture, heat, strong oxidizers, acid chlorides, acid anhydrides.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, praseodymium oxide, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: September 1998