MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY, INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: (3-Glycidoxypropyl)trimethoxysilane

CATALOG NUMBER:RS428			PURITY: 97%

FORMULA:C9H20O5Si	FORMULA WEIGHT: 236.34

CAS #: (3-Glycidoxypropyl)trimethoxysilane: 2530-83-8

Methanol: 67-56-1

CHEMICAL FAMILY: Organosilane

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

# HAZARDOUS INGREDIENTS:	%

Title compound	>97	ACGIH(TLV): No data

OSHA/PEL: No data

Methanol	<3	ACGIH(TWA): 200ppm(skin)

OSHA/PEL: No data

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE:  Colorless liquid

FREEZING POINT: <-70(C		       BOILING POINT(oC):  290 (C

VAPOR PRESSURE:  120(C: 2mm	       SPECIFIC GRAVITY:  1.070

SOLUBILITY IN WATER: reacts

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 110oC (230(F)

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: CO2, foam, dry chemical, and water spray

SPECIAL FIRE FIGHTING PROCEDURES: Avoid eye and skin contact. Do not breathe fumes or inhale vapors.

UNUSUAL FIRE AND EXPLOSION HAZARDS: Irritating fumes and organic acid vapors may develop when material is exposed to elevated temperatures or open flame.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

INHALATION: Inhalation of vapors or particulates may irritate the respiratory tract.

Overexposure may produce coughing, headache and nausea.

SKIN CONTACT: May produce irritation or contact dermatitis, which may be delayed

several  hours. Prompt and through washing with soap and water will reduce or eliminate

potential  dermal effects.

EYE CONTACT: Will cause immediate or delayed severe eye irritation, experienced as

Discomfort or pain, tear production, inflammable of conjunctiva. Corneal injury may result.

Oral Toxicity: oral rat, LD50: 8,400mg/kg. Oral toxicity is associated with methanol, a

Hydrolysis product which causes nausea, vomiting, headache, visual effects including blindness.

Onset of symptoms may be delayed up to 48 hours.

Chronic Toxicity: Glycidoxypropyltrimethoxysilane has been found to be weakly mutagenic in

Ames in vitro screening. In vivo studies have shown that repeated exposure to this material,

even at otherwise toxic doses, does not cause any mutagenic events. No tumerogenic response

To the chronic recurrent application of the material to the skin of mice was observed.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove victim to fresh air and seek medical attention.

SKIN CONTACT: Flush skin with water, then wash with soap and water.

EYE CONTACT: Flush with flowing water for at least 15 minutes and consult physician then, 	get medical attention immediately.

INGESTION: Never give fluids or induce vomiting if patient is unconscious or having

convulsions. Get medical attention.

NOTE TO PHYSICIAN: This product reacts with water in the acid contents of the stomach to form methanol. The combination of visual disturbances, metabolic acidosis and formic acid in urine is evidence of methanol poisoning. The therapeutic intravenous administration of ethanol (10mls/hour) allows methanol to be preferentially oxidized and reduces production of methanol metabolites. Acidosis must be treated with intravenous administration of sodium bicarbonate and methanol elimination may be increased by hemodialysis, as indicated. Treatment should be based on blood methanol levels and acid-base balance.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Stable in sealed container

CONDITIONS TO AVOID: Combustible; avoid contact with heat, sparks or open flame.

INCOMPATIBILITY: Reacts with water and moisture in air liberating methanol. Can react

exothermically with amine.

HAZARDOUS DECOMPOSITION: Organic acid vapors

HAZARDOUS POLYMERIZATION: No data

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Cover spill with absorbent material. Transfer to a suitable container for disposal.

WASTE DISPOSAL: Incinerate.  Alternatively, absorbs onto clay or vermiculite and dispose of absorbent material as solid waste. Follow all chemical pollution control regulation.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Local exhaust.  Mechanical ventilation recommended.

RESPIRATORY PROTECTION: If exposure exceeds TLV air-supplied or combination organic vapor acid gas respirator.

PROTECTIVE GLOVES: Rubber, neoprene or nitrile gloves.

EYE/FACE PROTECTION: Use chemical goggles and face shield. Do not wear contacts.

HANDLING AND STORAGE: Store in sealed containers.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED: May 15, 2001