MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Titanium (IV) butoxide

CATALOG NUMBER: T806

FORMULA: Ti(OC4H9)4 	FORMULA WEIGHT: 340.35

TSCA:  listed in the TSCA inventory

CHEMICAL FAMILY: Alkoxide

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

CHEMICAL: Titanium butoxide

CAS #                     %                                       PEL                                       TLV

5593-70-4                100                                     Not established                     Not established

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: Colorless to yellow liquid, odor of n-butyl alcohol

MELTING POINT: -55oC	BOILING POINT: 310-314oC

VAPOR DENSITY: 11.7	SPECIFIC GRAVITY: 0.995

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: 170 F

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Flammable liquid.  Use alcohol foam, carbon dioxide or dry chemical extinguishing agents.

SPECIAL FIRE FIGHTING PROCEDURES: No special firefighting procedures needed.  Use normal procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame and chemical resistant clothing; hats, boots and gloves.  If without risk, remove material from fire area.  Cool container with water from maximum distance.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

ACUTE EFFECTS

INGESTION: Abdominal pain, CNS depression

SKIN CONTACT: Local irritation

EYE CONTACT: Local irritation

INHALATION: Local irritation

MOST LIKELY ROUTE OF ENTRY: Skin contact

FIRST AID

In case of eye contact, immediately flush eyes with copious amounts of water for at least 15 minutes. In case of skin contact, immediately wash skin with soap and copious amounts of water. If inhaled, remove to fresh air. If not breathing give artificial respiration. If breathing is difficult, give oxygen. If swallowed, wash out mouth with water provided person is conscious. Call a physician. Remove and wash contaminated clothing promptly.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Oxidizers, acids, water.

HAZARDOUS DECOMPOSITION PRODUCTS: Decomposition may result in TiO2, CO, CO2, C4H9OH, and other toxic fumes.

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  September, 2010