MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-------------------------------------

CHEMICAL NAME: Ytterbium isopropoxide, 99%

CATALOG NUMBER: Y104-1	PURITY: 99+%

FORMULA: Yb(OC3H7i)3	FORMULA WEIGHT: 350.23

TSCA: not listed in the TSCA inventory	isopropanol: listed

CHEMICAL FAMILY: Metal alkoxide

-------------------------------------HAZARDOUS INGREDIENTS-------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	100 	ACGIH(TLV): No data

OSHA/PEL: No data

------------------------------------------------PHYSICAL DATA--------------------------------------

APPEARANCE AND ODOR: Light yellow powder

MELTING POINT: 200oC

BOILING POINT SUBL.:  190-200oC/.2mm

SOLUBILITY IN WATER: Reacts with water

--------------------------------------------------FIRE HAZARD----------------------------------------

FLASH POINT: No data

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Carbon dioxide, sand or foam but not with water

SPECIAL FIRE FIGHTING PROCEDURES: Ytterbium compounds have moderate fire hazard, in  the form of dust, when reacted with air, halogens.  Combustible.  If involved in a fire or heated to high temperatures, the material may burn.  Burning material may release toxic and corrosive fumes.  Leave area unless fitted with a self-contained breathing apparatus and fire protective clothing.

UNUSUAL FIRE OR EXPLOSION HAZARDS:  Combustible material.  No unusual fire or explosion hazards.  React with water or steam to produce flamming vapors.

-----------------------------------------------HEALTH HAZARD-------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

As a lanthanon, ytterbium may have an anti-coagulant action on blood.

INHALATION: May cause irritation of the nose and throat.

SKIN CONTACT: May cause irritation with stinging and burning sensations.

EYE CONTACT: Avoid eye contact.

INGESTION: High THR via ip route and moderate via oral route.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA-----------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY:  Water, mineral acid and oxidizing agents.

HAZARDOUS DECOMPOSITION PRODUCTS:  Isopropanol, ytterbium oxide, organic fumes, CO and CO2

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION-------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

----------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  October 1996