MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

19365 Business Center Drive, Suite 8 & 9

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Yttrium isopropoxide, 5g/100ml in toluene-isopropanol

CATALOG NUMBER: Y204	PURITY: 99+%

FORMULA: Y(OC3H7i)3	FORMULA WEIGHT: 266.17

TSCA: not listed in the TSCA inventory	isopropanol: listed 	toluene: listed

CHEMICAL FAMILY: Metal alkoxide solution

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	      %

Title compound, CAS#: 2172-12-5	           5 	ACGIH(TLV): No data

OSHA/PEL: No data

Isopropanol	, CAS#: 67-63-0              40-50       ACGIH(TLV): 400 ppm

OSHA/PEL: 400 ppm

Toluene, CAS#: 108-88-3                  55-45       ACGIH(TLV): 50ppm

OSHA/PEL: 200ppm

------------------------------------------------PHYSICAL DATA-----------------------------------------------

APPEARANCE AND ODOR: Yellowish liquid

MELTING POINT: No data	BOILING POINT: No data

VAPOR PRESSURE: No data	SPECIFIC GRAVITY: No data

SOLUBILITY IN WATER: Decomposes in water

--------------------------------------------------FIRE HAZARD-------------------------------------------------

FLASH POINT: No data

AUTOIGNITION TEMPERATURE: No data

EXTINGUISHING MEDIA: Flammable liquid.  Use alcohol foam, carbon dioxide or dry chemical extinguishing agents.  Water may be used to keep fire exposed containers cool.

SPECIAL FIRE FIGHTING PROCEDURES: Flammable liquid.  Material readily ignited with flame, sparks, friction or heat.  Burning material may release toxic and corrosive fumes.  Vapors can flow along surfaces to distant ignition sources and flash back.  Use normal fire fighting procedures which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame, and chemical resistant clothing; hats, boots, and gloves.  Leave the area unless fitted with a self-contained breathing apparatus and fire protective clothing..

UNUSUAL FIRE OR EXPLOSION HAZARDS: Flammable liquid.  Vapors can form explosive mixtures with air.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

MODE OF ENTRY:

INHALATION: Yes

SKIN CONTACT: Yes

EYE CONTACT: Yes

INGESTION: Yes

CARCINOGENCITY:

NTP: Not known

IARC: Not known

OSHA: Not known

EFFECTS OF OVEREXPOSURE:

Yttrium: may have an anticoagulant effect on the blood

Yttrium oxide: capable of causing death or permanent injury due to the exposures of normal use; incapacitating and poisonous via intraperitoneal route.  intraperitoneal LD50 (rat) = 500 mg/kg.

INHALATION: May cause irritation of the nose and throat.  Exposure to high concentrations has a narcotic effect, producing symptoms of drowsiness, headache, staggering, unconciousness, and possibly death.  Inhalation of 200ppm of toluene for 8 hrs. may cause impairment of coordination and reaction time; with higher concentration (up to 800ppm) these effects are increased and are observed in a shoter time.

SKIN CONTACT: May cause irritation with stinging and burning sensations.  Causes defatting of the skin.

EYE CONTACT: Vapors may irritate the eyes.  Splashes may cause severe irritation, possible corneal burns and eye damage.

INGESTION: Isopropyl alcohol may cause drowsiness, unconsciousness and death.  Gastrointestinal pain, cramps, nausea, vomiting, and diarrhea may also result.  The single lethal dose of isopropanol for a human adult is about 250 ml.

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Remove the victim to fresh air and seek medical attention if coughing, shortness of breath or irritation persists.

SKIN CONTACT: Wash the affected area with soap and water for at least 5 minutes.

EYE CONTACT: Immediately flush eyes, including under eyelids, with large amounts of water for at least 15 minutes.  Call a physician.

INGESTION: Give the victim plenty of water and seek immediate medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Moisture-sensitive material.

CONDITIONS TO AVOID: Contact with ignition source or heat.

INCOMPATIBILITY: Moisture, heat, strong oxidizers, acetaldehyde, chlorine, ethylene oxide, hydrogen-palladium combination, nitroform, phosgene, hydrogen peroxide-sulfuric acid combination, potssium tert-butoxide, hypochlorous acid, isocyanates, oleum, perchloric acid, aluminum isopropoxide, crotonaldehyde, (H2SO4 + HNO3), N2O4, AgClO4.

HAZARDOUS DECOMPOSITION PRODUCTS: CO, CO2, yttrium oxide, and organic fumes

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Wearing full protective equipment, eliminate all sources of ignition.  Cover spill with dry sand or vermiculite.  Sweep up the mixture and dispose of properly.

WASTE DISPOSAL: Consult state, local, or federal EPA regulations for proper disposal.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Glove bag or box with dry, inert atmosphere.

RESPIRATORY PROTECTION: NIOSH/MSHA approved respirator with an organic vapor cartridge.

PROTECTIVE GLOVES: Rubber

EYE/FACE PROTECTION: ANSI approved safety goggles

HANDLING AND STORAGE: Handle and store the material under an inert atmosphere of nitrogen or argon.  Keep away from heat.

OTHER PRECAUTIONS: The material will react with air and moisture.  Lab coat and apron, flame and chemical resistant coveralls, eyewash capable of sustained flushing, safety drench shower and hygienic facilities for washing.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology, Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  Nov. 2009