MATERIAL SAFETY DATA SHEET

CHEMAT TECHNOLOGY INC.

9036 Winnetka Avenue

Northridge, CA 91324

(818) 727-9786, (818) 727-9477 FAX

-----------------------------------------------IDENTIFICATION-----------------------------------------------

CHEMICAL NAME: Zinc (2,2,6,6-tetramethyl-3,5-heptanedionate)

CATALOG NUMBER:Z134

FORMULA: Zn(C11H19O2)2	FORMULA WEIGHT: 431.93

CHEMICAL FAMILY: Metal beta-diketonate compleses

CAS#: 14363-14-5

-------------------------------------HAZARDOUS INGREDIENTS---------------------------------------

HAZARDOUS INGREDIENTS:	%

Title compound	>99.9	ACGIH(TLV): No data

OSHA/PEL: No data

------------------------------------------------PHYSICAL DATA-----------------------------------------------

Boiling point:no data		                                    Melting point: 144(C

Specific gravity: not determined			Vapor pressure: @ N/A

Vapor Density: N/A					Solubility in water: reacts

%volatiles: N/A					Evaporation rates: N/A

Molecular weight: 431.93			            Other: N/A

Appearance and odor: off-white powder

--------------------------------------------------FIRE HAZARD-------------------------------------------------

Flash point, COC:N/A			Autoignition Temp.: N/A

Flammability Limits-LEL: N/A	UEL: N/A

Extinguishing media: Alcohol resistant foam, carbon dioxide, dry chemical.

Special fire fighting procedures: Avoid water spray as t-amyl alcohol will be generated.

Avoid eye and skin contact. Do not breathe fumes or inhale vapors.

Unusual fire and explosion hazards: irritating fumes and organic acid vapors may develop when material is exposed to elevated temperatures or open flame.

-----------------------------------------------HEALTH HAZARD----------------------------------------------

EYE CONTACT: May cause immediate or delayed severe eye irritation.

SKIN CONTACT: May produce irritation or contact dermatitis.  Prompt and thorough washing with soap and water will reduce or eliminate potential dermal effects.

INHALATION: Inhalation of dust or particulates may irritate the respiratory tract.

ORAL TOXICITY: not determined

CHRONIC TOXICITY: not determined

EMERGENCY AND FIRST AID PROCEDURES:

INHALATION: Move exposed individual to fresh air.  Administer oxygen if needed.  Call a physician.

SKIN CONTACT: Flush with water, then wash with soap and water.

EYE CONTACT: In case of contact, immediately flush eyes with flowing water for at least 15 minutes.  Get medical attention.

INGESTION: Never give fluids or induce vomiting if patient is unconscious or having convulsions.  Get medical attention.

-----------------------------------------------REACTIVITY DATA--------------------------------------------

STABILITY: Stable

CONDITIONS TO AVOID: Contact with oxidizers.

INCOMPATIBILITY: Moisture, heat, strong oxidizers

HAZARDOUS DECOMPOSITION PRODUCTS: Zinc odixe and organic acid vapors

HAZARDOUS POLYMERIZATION: None

---------------------------------ENVIRONMENTAL INFORMATION--------------------------------

SPILL OR LEAKAGE PROCEDURES: Utilize non-flammable absorbant, then sweep material and transfer to a suitable container for disposal.

WASTE DISPOSAL: After absorption onto non-flammable absorbent, dispose of as solid waste.  Follow all chemical pollution control regulations.

----------------------------------PROTECTION AND PRECAUTIONS--------------------------------

VENTILATION REQUIREMENTS: Local exhaust is recommended.  Mechanical is recommended.

RESPIRATORY PROTECTION: If exposure exceeds TLV, NIOSH approved dust and mist respirator.

PROTECTIVE EQUIPMENT: Rubber gloves, neoprene or nitrile gloves.  An eyewash and emergency shower should be available.  Launder clothing before reuse.

EYE/FACE PROTECTION: ANSI approved safety goggles

OTHER PRECAUTIONS: For research use only/ Store in sealed containers.

---------------------------------------------------------------------------------------------------------------------------

The information herein is believed to be accurate and reliable as of the date compiled.  However, Chemat Technology Inc. makes no representation, warranty or guarantee of any kind with respect to the information on this data sheet or any use of the product based upon this information.

DATE PREPARED:  May 24, 2005